## Slide 1: Daily Drilling Report 1.2.0 Elements
Yao Bo Lu
Stavanger, 11.05.2011

## Slide 2: Header
Daily Drilling Report 1.2.0 Elements, Yao Bo Lu, 11/05.2011
<number>
© 2010 Capgemini. All rights reserved.

## Slide 3: Report No
reportNo
Type: positiveCount
minOccurs: 0
maxOccurs: 1
Description: Sequence number of daily drilling report
Example input value: 1
Example output value: 1
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 4: Tight well
Name: tightWell
Type: logicalBoolean
minOccurs: 0
maxOccurs: 1
Description: Indicates if a well is tight or not.
Example input value: true
Example output value: yes
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 5: High pressure – high temperature
Name: hpht
Type: logicalBoolean
minOccurs: 0
maxOccurs: 1
Description: Indicates if a well is classified as HPHT (High pressure – high temperature)
Example input value: true
Example output value: yes
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 6: Pressure
Name: avgPresBH
Type: pressureMeasurePsig
minOccurs: 0
maxOccurs: 1
Description: Average bottomhole pressure (psig)
Example input value: 25
Example output value: 23
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 7: Temperature
Name: avgTempBH
Type: thermodynamicTemperatureMeasureCelsius
minOccurs: 0
maxOccurs: 1
Description: Average bottomhole temperature(c)
Example input value: 25
Example output value: 25
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 8: Fixed rig
Name: fixedRig
Type: logicalBoolean
minOccurs: 0
maxOccurs: 1
Description: Indicates if a rig is fixed or not
Example input value: true
Example output value: yes
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 9: Water depth
Name: waterDepth
Type: lengthMeasureMetre
minOccurs: 0
maxOccurs: 1
Description: Water depth in Mean sea level (m).
Example input value: 150
Example output value: 150
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 10: Period
Type: Calculated field
Example output value: 2006-06-06 00:00 - 2006-06-06 12:00
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 11: Operation
Daily Drilling Report 1.2.0 Elements, Yao Bo Lu, 11/05.2011
<number>
© 2010 Capgemini. All rights reserved.

## Slide 12: Start depth
Name: mdHoleStart
Type: measuredDepthCoord
minOccurs: 0
maxOccurs: 1
Description: Meassured depth at start of the activity (m).
Example input value: 150
Example output value: 150
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 13: End depth
Name: md
Type: measuredDepthCoord
minOccurs: 0
maxOccurs: 1
Description: Meassured depth at end of the activity (m).
Example input value: 150
Example output value: 150
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 14: Depth
Type: Calculated field
Example output value: 150
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 15: Main - Sub Activity
Name: proprietaryCode
Type: ActivityCodeNPD
minOccurs: 1
maxOccurs: 1
Description: Meassured depth at end of the activity (m).
Example input value: drilling -- drill
Example output value: drilling -- drill
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 16: State
Name: state
Type: MainActivityEvaluation
minOccurs: 1
maxOccurs: 1
Description: Finish, interrupted, failed, etc.
Example input value: ok
Example output value: ok
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 17: Bit record
Daily Drilling Report 1.2.0 Elements, Yao Bo Lu, 11/05.2011
<number>
© 2010 Capgemini. All rights reserved.

## Slide 18: Hours drilled
Name: eTimOpBit
Type: timeMeasureHour
minOccurs: 0
maxOccurs: 1
Description: Operating time spent by bit during the reporting period.
Example input value: 5
Example output value: 5
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 19: MD Start
Name: mdHoleStart
Type: measuredDepthCoord
minOccurs: 0
maxOccurs: 1
Description: Measured depth at start of reporting period.
Example input value: 150
Example output value: 150
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 20: MD end
Name: mdHoleEnd
Type: measuredDepthCoord
minOccurs: 0
maxOccurs: 1
Description: Measured depth at end of reporting period.
Example input value: 150
Example output value: 150
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 21: Dull grade
Name: dullGrade
Type: str32
minOccurs: 0
maxOccurs: 1
Description: Finish, interrupted, failed, etc.
Example input value: 2/3/NO/A/X/I/NO/DTF
Example output value: 2/3/NO/A/X/I/NO/DTF
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 22: Hole Made (Last 24H)
Type: Calculated field
Example output value: 15
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 23: Hours drilled (Last 24H)
Name: eTinOpBit
Type: timeMeasureHour
minOccurs: 0
maxOccurs: 1
Description: Operating time spent by bit during the reporting period.
Example input value: 5
Example output value: 5
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 24: ROP (Last 24H)
Name: ropAv
Type: velocityMeasureMetresPerHour
minOccurs: 0
maxOccurs: 1
Description: Average rate of penetration through Interval.
Example input value: 15
Example output value: 15
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 25: Total Hole Made
Name: mdTotHoleMade
Type: measuredDepthCoord
minOccurs: 0
maxOccurs: 1
Description: Total accumulated Measured depth for the entire run.
Example input value: 150
Example output value: 150
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 26: Total hours drilled
Name: totHrsDrilled
Type: timeMeasureHour
minOccurs: 0
maxOccurs: 1
Description: Total accumulated Hours of drilling for the entire run.
Example input value: 5
Example output value: 5
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 27: Total ROP
Name: totRop
Type: velocityMeasureMetresPerHour
minOccurs: 0
maxOccurs: 1
Description: Total accumulated Rate of penetration for the entire run.
Example input value: 15
Example output value: 15
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 28: Casing/Liner/Tubing information
Daily Drilling Report 1.2.0 Elements, Yao Bo Lu, 11/05.2011
<number>
© 2010 Capgemini. All rights reserved.

## Slide 29: Type of pipe
Name: type
Type: tubularTypes
minOccurs: 0
maxOccurs: 1
Description: The type of tubular (e.g., casing, tubing, liner, packer, open hole, other).
Example input value: c
Example output value: casing
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 30: Nominal outside diameter
Name: od
Type: lengthMeasureInch
minOccurs: 0
maxOccurs: 1
Description: The outside diameter of the tubular used.
Example input value: 5
Example output value: 5
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 31: Nominal inside diameter
Name: id
Type: lengthMeasureInch
minOccurs: 0
maxOccurs: 1
Description: The inside diameter of the tubular used.
Example input value: 5
Example output value: 5
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 32: Nominal Weight
Name: weight
Type: massPerLengthMeasurePoundsMassPerFoot
minOccurs: 0
maxOccurs: 1
Description: The weight per length of the tubular.
Example input value: 15
Example output value: 15
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 33: Nominal Grade
Name: grade
Type: str32
minOccurs: 0
maxOccurs: 1
Description: A 'code string class' that is representing members of 'API 5CT 7th. edition grade class'
Example input value: 15
Example output value: 15
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 34: Nominal Connection
Name: connection
Type: str32
minOccurs: 0
maxOccurs: 1
Description: A 'code string class' that is a standardrised set of strings used in a 'daily drilling report' to identify a member of 'daily drilling report connection class'
Example input value: 15
Example output value: 15
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 35: Length
Name: length
Type: lengthMeasureMetre
minOccurs: 0
maxOccurs: 1
Description: Length measured along string.
Example input value: 15
Example output value: 15
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 36: Top/Hangar
Name: mdTop
Type: measuredDepthCoord
minOccurs: 0
maxOccurs: 1
Description: The measured depth of the top of the tubular.
Example input value: 150
Example output value: 150
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 37: Bottom/Shoe
Name: mdBottom
Type: measuredDepthCoord
minOccurs: 0
maxOccurs: 1
Description: The measured depth of the bottom of the tubular.
Example input value: 150
Example output value: 150
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 38: Casing type
Name: casingType
Type: casingTypes
minOccurs: 0
maxOccurs: 1
Description: The casing type used in this tubular job stage.
Example input value: 15
Example output value: 15
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 39: Run Time
Name: dTimStart
Type: timestamp
minOccurs: 0
maxOccurs: 1
Description: Date time of start of this stimulation stage.
Example input value: 2011-02-07T12:00:00.000Z
Example output value: 12:00
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 40: End Time
Name: dTimEnd
Type: timestamp
minOccurs: 0
maxOccurs: 1
Description: Total accumulated Rate of penetration for the entire run.
Example input value: 2011-02-07T12:00:00.000Z
Example output value: 12:00
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 41: Description
Name: description
Type: descriptionString
minOccurs: 0
maxOccurs: 1
Description: Total accumulated Rate of penetration for the entire run.
Example input value: Lorem ipsum dolor sit amet, consectetur adipiscing elit. Praesent porttitor condimentum mi nec dictum. Quisque sodales lacinia lobortis. Donec interdum. Example output value: Lorem ipsum dolor sit amet, consectetur adipiscing elit. Praesent porttitor condimentum mi nec dictum. Quisque sodales lacinia lobortis. Donec interdum.
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 42: Cement information
Daily Drilling Report 1.2.0 Elements, Yao Bo Lu, 11/05.2011
<number>
© 2010 Capgemini. All rights reserved.

## Slide 43: Start Time
Name: dTimPumpStart
Type: timestamp
minOccurs: 0
maxOccurs: 1
Description: Datetime at start of pumping cement.
Example input value: 2011-02-07T12:00:00.000Z
Example output value: 12:00
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 44: End Time
Name: dTimPumpEnd
Type: timestamp
minOccurs: 0
maxOccurs: 1
Description: Datetime at end of pumping cement.
Example input value: 2011-02-07T12:00:00.000Z
Example output value: 12:00
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 45: Job type
Name: jobType
Type: cementJobTypes
minOccurs: 0
maxOccurs: 1
Description: Type of cement job.
Example input value: squeeze
Example output value: squeeze
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 46: Casing string diameter
Name: casingStrDia
Type: lengthMeasureInch
minOccurs: 0
maxOccurs: 1
Description: Casing string diameter of the casing cement (in).
Example input value: 5
Example output value: 5
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 47: Top plug used
Name: topPlug
Type: logicalBoolean
minOccurs: 0
maxOccurs: 1
Description: Top plug used? Values are "true" (or "1") and "false" (or "0").
Example input value: true
Example output value: yes
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 48: Bottom plug used
Name: botPlug
Type: logicalBoolean
minOccurs: 0
maxOccurs: 1
Description: Bottom plug used. Values are "true" (or "1") and "false" (or "0").
Example input value: true
Example output value: yes
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 49: Plug bumped
Name: plugBumped
Type: logicalBoolean
minOccurs: 0
maxOccurs: 1
Description: Plug bumped? Values are "true" (or "1") and "false" (or "0").
Example input value: true
Example output value: yes
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 50: Plug bump pressure
Name: presBump
Type: pressureMeasure
minOccurs: 0
maxOccurs: 1
Description: Pressure plug bumped.
Example input value: 15
Example output value: 15
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 51: Float held
Name: floatHeld
Type: logicalBoolean
minOccurs: 0
maxOccurs: 1
Description: Float held? Values are "true" (or "1") and "false" (of "0").
Example input value: true
Example output value: yes
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 52: Pressure release time
Name: eTimPresRelease
Type: timestamp
minOccurs: 0
maxOccurs: 1
Description: Time pressure Release
Example input value: 2011-02-07T12:00:00.000Z
Example output value: 2011-02-07 12:00
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 53: Full returns
Name: annFlowAfter
Type: logicalBoolean
minOccurs: 0
maxOccurs: 1
Description: Fluid returns. Values are "true" (or "1") and "false" (or "0").
Example input value: true
Example output value: yes
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 54: Cement volume returns
Name: volReturns
Type: volumeMeasureCubicMetre
minOccurs: 0
maxOccurs: 1
Description: Volume of returns.
Example input value: 15
Example output value: 15
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 55: Reciprocated
Name: reciprocated
Type: logicalBoolean
minOccurs: 0
maxOccurs: 1
Description: Pipe being reciprocated. values are "true"(1) and "false"(0).
Example input value: true
Example output value: yes
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 56: Rotated
Name: rotated
Type: logicalBoolean
minOccurs: 0
maxOccurs: 1
Description: Casing string being rotated. Values are "true(1) and "false"(0).
Example input value: true
Example output value: yes
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 57: Comments
Name: comments
Type: commentString
minOccurs: 0
maxOccurs: 1
Description: Comments for a cement job.
Example input value: Lorem ipsum dolor sit amet, consectetur adipiscing elit. Praesent porttitor condimentum mi nec dictum. Quisque sodales lacinia lobortis. Donec interdum.
Example output value: Lorem ipsum dolor sit amet, consectetur adipiscing elit. Praesent porttitor condimentum mi nec dictum. Quisque sodales lacinia lobortis. Donec interdum.
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 58: Fluid Type
Name: typeFluid
Type: fluidTypes
minOccurs: 0
maxOccurs: 1
Description: Fluid type: Mud, Wash, Spacer, Slurry.
Example input value: 2011-02-07T12:00:00.000Z
Example output value: 12:00
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 59: Volume pumped
Name: volPumped
Type: volumeMeasureCubicMetre
minOccurs: 0
maxOccurs: 1
Description: Volume Pumped.
Example input value: 15
Example output value: 15
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 60: Fluid density
Name: density
Type: densityMeasure
minOccurs: 0
maxOccurs: 1
Description: Fluid density
Example input value: 15
Example output value: 15
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 61: Yield point
Name: yp
Type: specificVolumeMeasureCubicFeetPer94PoundSack
minOccurs: 0
maxOccurs: 1
Description: Yield point (Bingham and Herschel Bulkley models).
Example input value: 15
Example output value: 15
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 62: Mix water ratio
Name: ratioMixWater
Type: specificVolumeMeasureUsGallonsPerSack94
minOccurs: 0
maxOccurs: 1
Description: Mix water ratio.
Example input value: 15
Example output value: 15
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 63: Free water
Name: pcFreeWater
Type: volumePerVolumeMeasurePercent
minOccurs: 0
maxOccurs: 1
Description: Test free water na: = mL/250ML.
Example input value: 15
Example output value: 15
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 64: Thick time
Name: eTimThickening
Type: timeMeasureHour
minOccurs: 0
maxOccurs: 1
Description: Test thickening time.
Example input value: 5
Example output value: 5
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 65: Fluid description
Name: descFluid
Type: descriptionString
minOccurs: 0
maxOccurs: 1
Description: Fluid description
Example input value: Lorem ipsum dolor sit amet, consectetur adipiscing elit. Praesent porttitor condimentum mi nec dictum. Quisque sodales lacinia lobortis. Donec interdum. Example output value: Lorem ipsum dolor sit amet, consectetur adipiscing elit. Praesent porttitor condimentum mi nec dictum. Quisque sodales lacinia lobortis. Donec interdum.
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 66: Comments
Name: comments
Type: commentString
minOccurs: 0
maxOccurs: 1
Description: Comments for cementing fluid.
Example input value: Lorem ipsum dolor sit amet, consectetur adipiscing elit. Praesent porttitor condimentum mi nec dictum. Quisque sodales lacinia lobortis. Donec interdum. Example output value: Lorem ipsum dolor sit amet, consectetur adipiscing elit. Praesent porttitor condimentum mi nec dictum. Quisque sodales lacinia lobortis. Donec interdum.
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 67: Perforation Information
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 68: Duration Well Perf
Type: Calculated field
Example output value: 15H
Insert "Title, Author, Date"
<number>
© 2010 Capgemini. All rights reserved.

## Slide 69: More information
Daily Drilling Report 1.2.0 Elements, Yao Bo Lu, 11/05.2011
<number>
© 2010 Capgemini. All rights reserved.
Please contact:
Stein Arve Finnestad stein-arve.finnestad@capgemini.com
Yao Bo Lu yao-bo.lu@capgemini.com